## Slide 1: Retinal photo: quick guide
Dilate pupils, repeat
Repeat
Repeat
Clean lens, repeat
Too dark
Blurred
Not aligned
Artefact
FAILED IMAGES
GOOD APPROACH
Clean lens daily (lens cloth)
Correct chair/table height
Dark setting
Cloth over the head
Guide patient through procedure
GOOD IMAGE
Good brightness
Sharp focus (vessels)
Good position (fovea + disc)
No artefacts
>90% images should be perfect
IF IN DOUBT CHECK WITH TEAM MANAGER
PRINT THIS PAGE AND DISPLAY AT EYE STATION

## Slide 2: Retinal photo: correct seating height
Eyes in line with canthus mark
Forehead pressed firmly against forehead rest
Participant fully seated and comfortable on chair
Adjust seating height of the participant such that participant can comfortably achieve the following:
Canthus mark

## Slide 3: Retinal photo: cleaning instructions
Cleaning of lens
Obtain lens cleaning cloth or paper (e.g. UVEX Lens cleaning tissues or similar) and diluted Acetone or Lens cleaning solution
Wet the lens paper with cleaning solution and wipe the Ocular Lens with one pass in one direction. If using lens paper, discard the used lens paper
Use a new sheet for each repeat cleaning until the Ocular Lens is clean
Chinrest and forehead rest
Soak a cleaning cloth or towel in disinfecting solution or use a wet isopropyl alcohol cleaning paper pad
Wipe the chinrest and forehead rest with the cleaning towels or paper pad before or after use.
If the chinrest paper is used, remove one piece for each patient.